Soldering
FabAcademy 2022 Bootcamp

---
Index
- Some concepts
  - Soldering / Welding
- Some components
  - Printed Circuit Board (PCB)
  - Through-Hole
  - Surface Mount Device (SMD)
  - Soldering iron
- Soldering

---
Soldering / Welding
- Soldering (US: /ˈsɒdərɪŋ/; UK: /ˈsoʊldərɪŋ/) is a process that joins metals by melting and putting a filler metal (solder) into the joint, the filler metal having a lower melting point than the adjoining metal.
- Welding is a process that joins metals by using high heat to melt the parts together and allowing them to cool, causing fusion.

---
Printed Circuit Board
- Base board (typically made from fiber glass (FR-4))
- Copper traces on top and bottom
  - Created by chemically removing superfluous copper
  - Created by mechanically removing superfluous copper
- Solder mask to protect traces
- Silk screen for identification (text)

---
Through hole
- Leads of a component are stuck through a hole in the PCB
- Easy to solder by hand (large components)
- Hard to solder by machine

---
Surface Mount Device
- Leads of a component are placed on a pad on the same side of the PCB (no hole)
- Hard(-er) to solder by hand (small components)
- Easy to solder by machine (reflow oven / wave)

---
Solder
- Metal alloy
  - Early days 60/40 = 60% Sn / 40% Pb
  - Nowadays 99.3/0.7 = 99.3% Sn / 0.7% Cu
- Flux added
  - Helps with removing oxide from metal
  - This is the smokey bit

---
Soldering iron
- Hot tip
- Hot air

---
Through-hole soldering

---
Through-hole soldering

---
Through-hole soldering

---
Through-hole soldering

---
SMD Soldering

---
SMD Soldering

---
SMD Soldering

---
SMD Soldering

---
When things go wrong...
Image: www.leadsintec.com

---
Some tips
- Temperature soldering iron depends on solder
  - Typically 325 - 350 °C
- Heat pad and component
- Adding flux can help
  - Drag solder
  - Large surfaces
- Safety tip →

---
Exercise
https://fabacademy.org/2021/labs/waag/students/kooi-erwin/course-2022/solder-exercise/