Electronic design
FabAcademy 2024

---
Index
- Some concepts
  - System / Circuit
  - Voltage / Current / Power
- Some components
  - Resistors
  - Capacitors / Coils
  - Diodes / LEDs
  - Transistors
  - Microcontrollers
- Measuring
  - Multimeter
  - Oscilloscope
  - Logic Analyser
- Designing
  - KiCAD schematic
  - KiCAD pcb
- Hello World!

---
System
System
Input
Output

---
Circuit
A circuit is a closed loop where electrons can flow

---
Voltage (V, Volt)
- Difference in electrical potential between points
- Sum of all voltages around a loop = 0
- Water analogy:
Angel Falls, Venezuela
Niagara Falls, Canada

---
Current (I, Ampere)
- Amount of flowing electrons (SI unit)
- Sum of all currents in a node = 0
- Water analogy:
Angel Falls, Venezuela
Niagara Falls, Canada

---
Current (I, Ampere)
- Direct current
- Alternating current

---
Power (P, Watt)
- P = V * I
- Energy is Power * time (e.g. kWh)
- Water analogy:
Angel Falls, Venezuela
Niagara Falls, Canada

---
Index
- Some concepts
  - System / Circuit
  - Voltage / Current / Power
- Some components
  - Resistors
  - Capacitors / Coils
  - Diodes / LEDs
  - Transistors
  - Microcontrollers
- Measuring
  - Multimeter
  - Oscilloscope
  - Logic Analyser
- Designing
  - KiCAD schematic
  - KiCAD pcb
- Hello World

---
Resistor (R, Ω, Ohm)
- A current-limiter
- One of the most important components
- R = V / I
- No polarity

---
Resistor (R, Ω, Ohm)
- Water analogy
- Symbol

---
Resistor (R, Ω, Ohm)

---
Capacitor (C, Farad)
- A storage tank for electric fields (charge)
- C = Q/V and I = C dV/dt
- Often used in filters
- “DC open, AC resistor”
- Can be unpolarized (ceramic, tantalum)
- Can be polarized (electrolytic)

---
Capacitor (C, Farad)
- Water analogy
- Symbol
- Behaviour

---
Diode / LED (D)
- One-way valve for electrons
- Often used as bridge rectifier
- Light Emitting Diode (LED)
- Color depends on elements used
- Also light sensitive

---
Diode / LED (D)
- Water analogy
- Symbol
- Behaviour

---
Diode / LED (D)
- Forward voltage
- Forward current
- LED example: VF = 2V1, I = 10mA, Source = 5V
- Calculate R and select common R
- Hint: R = V / I

---
Coil (L, Henry)
- A storage tank for magnetic fields
- L = V / dI/dt
- Also used in filters
- “DC short-circuit, AC resistor”
- Used in relays and motors
- Flyback diode

---
Transistor (Q)
- Amplifier and/or switch
- Bipolar: A small current can amplify a large current
- Bipolar: Ic = β * Ib where β = amplification factor
- MOSFET: A small voltage can drive a larger current

---
Transistor (Q)
- Water analogy
- Symbols

---
Microcontroller (U, IC)
- Integrated Circuit, built from transistors (mosfets)
- Programmable device with inputs, outputs, memory and calculation engine (ALU)
  - Digital inputs and outputs (I/O)
  - Analog inputs (ADC)
  - Analog outputs (DAC)
  - Digital interfaces (serial, i2c, spi, twi, updi, jtag, ...)
- Controlled by registers
- Microprocessor is just memory and ALU

---
Microcontroller (U, IC)
- “Arduino” = Atmel Atmega328p, 8 bit
- SAMD11C = ARM Cortex M0+, 32 bit
- ESP32 = Xtensa LX6 dual-core, 32 bit
- RP2040 = ARM Cortex M0+, 32 bit
- …

---
Index
- Some concepts
  - System / Circuit
  - Voltage / Current / Power
- Some components
  - Resistors
  - Capacitors / Coils
  - Diodes / LEDs
  - Transistors
  - Microcontrollers
- Measuring
  - Multimeter
  - Oscilloscope
  - Logic Analyser
- Designing
  - KiCAD schematic
  - KiCAD pcb
- Hello World

---
Multimeter
- Most useful measurement tool
  - Voltage
  - Current
  - Resistance
  - And more…
- There are no really bad multimeters

---
Multimeter
- Measures voltage across
- Measures current through
  - After converting it to a voltage
  - V = I / R → 1 Ohm resistor → V = I / 1 = I
- Remember to always reconfigure leads when done with current measurements!
- Remember to always check leads before use!

---
Oscilloscope
- Most versatile measurement tool
  - Multiple voltage in time domain
  - Frequency counter
- Hardware-based
- PC based (w/ DAC)

---
Logic analyzer
- “Oscilloscope” for digital signals
- Useful for showing the
  relation between
  multiple signals
- Decoding digital protocols

---
Logic analyzer

---
Index
- Some concepts
  - System / Circuit
  - Voltage / Current / Power
- Some components
  - Resistors
  - Capacitors / Coils
  - Diodes / LEDs
  - Transistors
  - Microcontrollers
- Measuring
  - Multimeter
  - Oscilloscope
  - Logic Analyser
- Designing
  - KiCAD schematic
  - KiCAD pcb
- Hello World!

---
KiCAD schematic
- Design your schematic
- Select symbolic components
- Connect components together with wires or busses
- Annotate components
- Assign values and footprints

---
KiCAD schematic

---
KiCAD schematic

---
KiCAD pcb
- Design your board
- Place physical components
- Connect components with traces
- Run connectivity tests and pre-production tests
- Generate production files

---
KiCAD pcb

---
KiCAD pcb

---
Group assignment
- use the test equipment in your lab to observe the operation of a microcontroller circuit board
- send a PCB out to a board house

---
Hello World! The curse of all modern software…
- use an EDA tool to design a development board to interact and communicate with an embedded microcontroller, produce it, and test it
- extra credit: try another design workflow
- extra credit: design a case for it
- extra credit: simulate its operation