Input Devices
FabAcademy 2024

---
System
System
Input
Output

---
Index
- Two types
  - Analog
  - Digital
- Interfacing
  - ADC
  - GPIO
  - Protocol
- Physical units
  - Temperature
  - Pressure
  - Magnetic fields
  - Motion
  - Distance
  - Resistance / Capacitance
  - ...

---
Two types – Analog
- The physical unit is converted to a resistance, capacitance or current (then to voltage)
- Values are sampled (taken over time)
- Signals can be amplified
  before sampling
Vout = Vin(1+ R2/R1)

---
Two types – Digital
The physical unit is converted in opening or closing a circuit

---
Index
- Two types
  - Analog
  - Digital
- Interfacing
  - ADC
  - GPIO
  - Protocol
- Physical units
  - Temperature
  - Pressure
  - Magnetic fields
  - Motion
  - Distance
  - Resistance / Capacitance
  - ...

---
Interfaces – ADC
- Analog to Digital Converter
- Voltage to value
- 8-bit (0-255), 10-bit (0-1023), 12-bit (0-4095)
- More bits, more resolution
- Value = AnalogRead(pin);

---
Interfaces – ADC
- How does it work?
- Resistor network
- Comparators
(source: https://microcontrollerslab.com/)

---
Interfaces – ADC
- 1V1 reference voltage in datasheet while VCC is 5V?
- Wheatstone bridge
- One resistor is variable
- Like a scale in balance
- Much more accuracy
  also with low resolution ADC

---
Interfaces – GPIO
- General Purpose Input-Output
- Low (0 to 1/3 VCC) / High (2/3 VCC to VCC)
  - There is an undefined between 1/3 VCC and 2/3 VCC
  - This can cause interesting problems
  - Use (uC-internal) pull-up resistors to force valid signals
- Value = DigitalRead(pin);

---
Interfaces – Protocol
- Typically two-way communication
- Address + Command to sensor
- Address + Value from sensor
- Often master/slave/multi-slave, (host/client/multi-client) configuration
- More details next week...

---
Interfaces – Protocol
- 1wire / TWI (Two Wire Interface)
- I2C (Inter-IC Communication)
- SPI (Serial Peripheral Interface)
- Serial
- PWM (Pulse Width Modulation)
- Hardware or bit-banging

---
Interfaces – Protocol
- 1wire / TWI
  - Invented by Dallas Semiconductor Corp.
  - VCC / DATA / GND
  - VCC + data / GND
  - Each sensor has a hard-coded 264-bit identifier
  - Famous:
    - DS18D20 temperature sensor
  - Also famous but different:
    - DTH11 temp/hum

---
Interfaces – Protocol
- I2C
  - Invented by Philips for communication inside TV set
  - 7-bit address for IC, most of them fixed
    - But nobody is stopping you...
  - Famous:
    - PCA9555 I/O expander
    - BME280 temp/hum
    - VL51L0X laser distance (Time-of-Flight)

---
Interfaces – Protocol
- SPI
  - Invented by Motorola
  - Exchange of bits between master – slave (MISO - MOSI)
  - Use Chip Select (CS) to specify which slave to talk to
  - Famous:
    - BME280 temp/hum …
    - DS1302 Real Time Clock
    - Flash memory/SD cards

---
Interfaces – Protocol
- Serial
  - Generic UART
  - Rx / Tx with a baudrate
  - Famous:
    - US-100 ultrasonic distance
    - NEO-8M GPS receiver
    - MH-Z19B CO2 concentration
  - Less famous, but also cool:
    - SI-3BM geiger-müller counter

---
Interfaces – Protocol
- PWM
  - Duty cycle
  - For use in EMC-noisy environments
  - Famous:
    - ...

---
Index
- Two types
  - Analog
  - Digital
- Interfacing
  - ADC
  - GPIO
  - Protocol
- Physical units
  - Temperature
  - Pressure
  - Magnetic fields
  - Motion
  - Distance
  - Resistance / Capacitance
  - ...

---
Units
- SI system
  - Second (s) for time
  - Meter (m) for length
  - Kilogram (kg) for mass
  - Ampere (A) for electric current
  - Kelvin (K) for thermodynamic temperature
  - Mole (mol) for amount of substance
  - Candela (cd) for luminous intensity

---
Units
- Everything else is derived
- Volt	= kg * m2 * s−3 * A−1 (or (kg * m2) / ( s3 * A))
  - Volt = Watt / Ampere (remember P = I * V)
  - Watt = Joule / second
  - Joule = Newton * meter
  - Newton = kg * meter / second / second (g=9.8 m * s−2)

---
PLay-time

---
Assignment
- Individual assignment:
  - measure something: add a sensor to a microcontroller board that you have designed and read it
- group assignment:
  - probe an input device's analog levels and digital signals