Networking and Communications
FabAcademy 2024

---
Index
- Connecting stuff
- Protocols
  - UART
  - SPI
  - I2C
- Bus pull-up
- Bus termination
- TCP/IP
  - Addresses
  - Subnet and beyond
  - over Ethernet
  - Services
- Play time!

---
Connecting stuff
- Getting data from here to there and back again
- From (lots of) sensors to microcontrollers to displays
- In FabAcademy networking often 1 main (µC) and multiple secondaries (sensors, LEDs, displays).

---
Connecting stuff
- Star topology
- Main has 1:1 connection to all secondaries
- Addressing is done by selecting a communication line
UART, SPI

---
Connecting stuff
- Ring topology
- Output of one secondary is connected to the input of the next secondary
- Addressing is done by its place in the ring
Neopixels, SPI

---
Connecting stuff
Bus topology
I2C, WiFi

---
Protocols – UART
- Asynchronous
  - No clock
  - Rx / Tx with a fixed speed
- Synchronization rules
  - 9600,8,n,1
    - 9600 baud (= bit/second)
    - 8 data bits
    - no parity bit
    - 1 stop bit

---
Protocols – UART
- Parity for 1-bit error detection (no correction)
  - P = d0 ⊕ d1 ⊕ d2 ⊕ d3 ⊕ d4 ⊕ d5 ⊕ d6 ⊕ d7
  - 0 for even
  - 1 for odd

---
Protocols – UART
- RS232
  - UART with +/- 15 V levels
- RS485
  - UART with differential signals
  - Full duplex (4 wires) / Half duplex (2 wires)

---
Protocols – UART
- Even better RS485
  - Differential signals + twisted wires for lower EMC

---
Protocols – UART
- Lame claim to fame: AVR’s MPCM
  - Multi Processor Communication Mode
  - 8-bit address with this-is-an-address bit
  - Upon receiving an address, each µC checks the address
  - Only the addressed µC switches to regular receive
  - All others remain in MPCM and wait till the next address
  - All implemented in hardware
    - limited interruption on running code
    - limited impact on memory and program size

---
Protocols – UART

---
Protocols – SPI
- Serial Peripheral Interface
- Invented by Motorola
- Exchange of data between
  main – secondary (MISO – MOSI)
- High data-rate
- Clock for data synchronization
  Use Chip Select (CS) to specify
  which receiver to talk to

---
Protocols – SPI
- Or use daisy-chaining to send
  all data in one stream to all
  receivers
- (same principle as NeoPixels)

---
Protocols – SPI
- Mode 0
  - CPOL 0
  - MOSI rising
  - MISO falling
- https://www.analog.com/en/analog-dialogue/articles/introduction-to-spi-interface.html

---
Protocols – SPI
- Fast, so often used for
  - flash memory
  - SD cards
  - displays
- Accelerometer in my Input Shaper Calibrator

---
Protocols – I2C
- Inter-IC Communication
- Invented by Philips
- 7-bit address mostly fixed
    - PCA9555
      - 0100<A2><A1><A0>R/W
      - 0100000x - 0100111x
    - But nobody is stopping you…
- 10-bit address also possible

---
Protocols – I2C
- Instead of just sending bits (like UART or SPI), addressing and an operation is required
- Receivers acknowledge successful reception
- Sender in control of the bus
- More elaborate protocols possible

---
Protocols – I2C
- https://learn.adafruit.com/working-with-i2c-devices
- https://www.analog.com/en/analog-dialogue/articles/i2c-communication-protocol-understanding-i2c-primer-pmbus-and-smbus.html

---
Bus pull-up / -down
- Good practice to fix bus levels
  to ensure a valid signals
- Best value depends on speed
- Rule of thumb:
  - SPI: 10kΩ pull-down (mode 0)
  - I2C: 4k7Ω pull-up

---
Bus termination
- Long communication wires (many meters) or wires carrying high frequency (many kHz) signals must be terminated to prevent reflections and provide a good impedance
- A wire acts as a capacitor with a resistor
  (low-pass filter)

---
Index
- Connecting stuff
- Protocols
  - UART
  - SPI
  - I2C
- Bus pull-up
- Bus termination
- TCP/IP
  - Addresses
  - Subnet and beyond
  - over Ethernet
  - Services

---
OSI layers
- 7 – application layer
- 6 – presentation layer
- 5 – session layer
- 4 – transport layer
- 3 – network layer
- 2 – datalink layer
- 1 – physical layer

---
TCP/IP
- Transmission Control Protocol / Internet Protocol
- Invented by DARPA for highly resilient communication
- IETF RFC’s

---
TCP/IP
- IP address (routable)
- Subnet
- Default gateway
- Underlaying: MAC addresses (not routable)

---
TCP/IP – Addresses
- IPv4
  - 95.216.151.48
  - Network Address Translation
    - 10.0.0.0/8
    - 172.16.0.0/12
    - 192.168.0.0/16
- IPv6
  - 2a10:3780:2:52:185:93:175:46

---
TCP/IP – Subnet and beyond
- Subnet determines scope of local network
  - Common subnetmask: 255.255.255.0 or /24
- Calculate if destination IP is local or not
- Example
  - 192.168.1.1/24 my IP
  - 95.216.151.48 destination IP

---
TCP/IP – Subnet and beyond
- Calculate if destination is local or not
  11000000.10101000.00000001.00000001 my IP
  11111111.11111111.11111111.00000000 subnet AND
  11000000.10101000.00000001.00000000 network addr
  01011111.11011000.10010111.01100000 destination IP
  11111111.11111111.11111111.00000000 subnet AND
  01011111.11011000.10010111.00000000 network addr

---
TCP/IP – Subnet and beyond
- Calculate if destination is local or not
  11000000.10101000.00000001.00000000
  01011111.11011000.10010111.00000000 XOR
  10011111.01110000.10010110.00000000
  - If not zero, then not local
  - Send packet to default gateway

---
TCP/IP – Subnet and beyond
- Default gateway
  - Knows where to ask for non-local IP addresses
  - An IP address on the local network

---
TCP/IP – over Ethernet

---
TCP/IP – over Ethernet
- MAC address (Media Access Control)
- Unique address for a network interface
  - Physical RJ45
  - WiFi
  - virtual
- ARP (Address Resolution Protocol) for finding link between IP address and MAC address
  - Who has 10.1.3.254? Tell c4:03:a8:86:a1:14
  - 10.1.3.254 is at 14:fe:b5:db:e6:ab

---
TCP/IP – Services
- ARP – Address Resolution Protocol
- BGP – Border Gateway Protocol
- DNS – Domain Name System
- DHCP – Dynamic Host Configuration Protocol
  - Beware the 169.254.0.0/16
- NTP – Network Time Protocol

---
Index
- Connecting stuff
- Protocols
  - UART
  - SPI
  - I2C
- Bus pull-up
- Bus termination
- TCP/IP
  - Addresses
  - Subnet and beyond
  - over Ethernet
  - Services
- Play time!

---
Assignment
- Individual assignment:
  - design, build, and connect wired or wireless node(s) with network or bus addresses and local input and/or output device(s)
- Group assignment:
  - send a message between two projects