Output devices
FabAcademy 2022

---
System
System
Input
Output

---
Index
- Lamp
- LED
  - RGB
- Display
  - 7-segment
  - Dot-matrix
  - LED, LCD and VFD
- Solenoid
- Speaker
  - Piezo
- Motor
  - DC
  - Servo
  - Stepper

---
Lamp
- Glowing filament in near-vacuum glass case
- Don’t use them
  - VERY inefficient in power use (+/- 5%)

---
LED
- Light Emitting Diode
- Color depends on used materials
  - Galliumaluminiumarsenide (AlGaAs) - red
  - Galliumarseenfosfide (GaAsP) - amber/yellow
  - Galliumfosfide (GaP) - green
  - Galliumnitride (GaN) - blue

---
LED
- Focused beam
- Clear or diffused casing (see nametag board)
- Forward voltage depends on used material
  - Red +/- 1V8
  - Yellow +/- 2V1
  - Green +/- 3V2
  - Checketh ye olde datasheet

---
LED
- Driving one LED from one µC pin?
  - Connected directly through a resistor (I < 50mA)
- Driving more LEDs from one pin?
  - Connected through a MOSFET or BJT
    (MOSFET is easier)

---
LED – RGB discrete
- Multiple colored LED’s in one case
- Controlled by PWM pulses

---
LED – RGB discrete
- Pulse Width Modulation
- Dedicated hardware in µC
  (timers and their registers)
- 100 Hz nice for LEDs
- 100 Hz nice for servo’s

---
LED – RGB digital
- Multiple colored LED’s in one case
- Integrated microcontroller
- Controlled by serial communication

---
Display – 7-segment

---
Display – 7-segment
- Dedicated 7-segment driver IC’s (ie MAX7219)
- Select the correct digit
- Translate binary to a-to-h
- Translate serial communication to a-to-h
- Can be cascaded

---
Display – Dot-matrix

---
Display – Dot-matrix
- Dedicated dot-matrix driver IC’s (ie. MAX7219 :-)
- Often integrated in display
- Controlled via parallel or serial communication
- Lots of Arduino libraries
  LCD.print(“Hello World!”);

---
Display – LED, LCD and VFD
- (O)LED
  - Turn on an LED to enable a segment / pixel
- LCD
  - Change the polarization of the display to reflect light
- VFD
  - Apply high voltage to ionize phosphor atoms
  - Popular in consumer electronica of the ‘90s

---
Index
- Lamp
- LED
  - RGB
- Display
  - 7-segment
  - Dot-matrix
  - LED, LCD and VFD
- Solenoid
- Speaker
  - Piezo
- Motor
  - DC
  - Servo
  - Stepper

---
Solenoid
- Coil of copper wire creates EM field
- Attracts bits of metal
- Relay or valve

---
Solenoid
- Solenoids want to preserve the magnetic field
  - Use fly-by diode
- Solenoids can draw a lot of current
  - Use MOSFET

---
Speaker
- Solenoid attached to a membrane
- 20Hz - 20kHz

---
Speaker – Piezo
Crystalline wafer that deforms when voltage is applied

---
Motor – DC
- Static magnet + Varying electromagnet
- More volt = more speed
- Direction of voltage =
  direction of motion

---
Motor – DC
- H bridge
- A = forward
- B = backward
- A + B = short circuit!
- Dedicated driver IC’s

---
Motor – Servo
- DC motor + gearbox + sensor = position control
- Location controlled via analog voltage (or PWM)

---
Motor – Stepper
Static magnet + Varying electromagnets at angles = precision motion (steps)

---
Motor – Stepper
Controlling via phased signals

---
Motor – Stepper
- Dedicated control circuits
- Controlled via serial
- Arduino library
  - setTargetPosition(100);
  - setTargetVelocity(2000000);

---
Motor – Stepper
Demo:
https://gitlab.cba.mit.edu/neilg/urumbu/-/tree/master/serialstep/serialstep-DRV8428P

---
Index
- Lamp
- LED
  - RGB
- Display
  - 7-segment
  - Dot-matrix
  - LED, LCD and VFD
- Solenoid
- Speaker
  - Piezo
- Motor
  - DC
  - Servo
  - Stepper

---
Measuring

---
Assignment
- group assignment:
  - measure the power consumption of an output device
- individual assignment:
  - add an output device to a microcontroller board you've designed, and program it to do something